## Slide 1: Digital systems
Dr. Iness NEDJI MILAT
iness.nedji@ensia.edu.dz
Number systems
Chapter 1

## Slide 2: Digital systems
Digital system is a combination of devices (most often electronic) designed to manipulate information that are represented in digital form (discrete values).
Some of the more familiar digital systems include digital computers,
Information processed by computer can be on different formats : number, text, image, audio, video,
All these formats are represented in numeric values (number systems),
In computer, they are always coded in binary form (BIT: BinarydigIT),
Bits : sequence of 0 and 1.

## Slide 3: Bits : Binary digITs
Computer systems do not represent numeric values using the decimal system but using binary system.
Computers are built around the idea of two states : true (1) and false (0).
Transistors represent this in hardware,
and bits represent this in software!
Gate
Drain
Source
Gate
Source
Drain
pMOS
nMOS
Bit (Binary digIT) is represented by two voltage levels, where any voltage between 0 and 0.2 V represents a 0 and any voltage between 0,9 and 1,1 Vrepresents a 1.

## Slide 4: Number systems
All data in digital systems are represented in number systems,
Many number systems are in use in digital technology. The most common are the decimal, binary, octal, and hexadecimal systems.
The decimal system is clearly the most familiar to us because it is a tool that we use every day.
Unsigned : 0, 1, 2, 3,,,,
Integer
real
Decimal number
Signed : ,,,,-2, -1, 0, 1, 2,,,,,
Fixed-point : 3.14
Floating-point : 3.14 = 31.4 * 10-1 = 0.0314 * 102

## Slide 5: Decimal System : base 10
The decimal system is called the base (radix)10 system because it has 10 digits (0,1,2,3,4,5,6,7,8,9)
The decimal system is a positional-value system in which the value of a digit depends on its position.
2
7
4
5
ones
Tens
hundreds
Thousands
100
101
102
103
10x
Weights:
2745= 2*103 + 7*102 + 4*101 + 5*100 (Polynomial representation)
2745.214 = 2*103 + 7*102 + 4*101 + 5*100 + 2*10-1 + 1*10-2 + 4*10-3
The 2 carries the most weight; it is referred to as the most significant digit (MSD).The 5 carries the least weight and is called the least significant digit (LSD).
For example :
MSD
LSD
Positional value

## Slide 6
1
1
0
1
Least significant bit (lsb)
The Binary Number System uses base (radix) 2.
It includes the digits 0 and 1.
For example:
twos
fours
eights
20
21
22
23
(1101)2 = 1*23 + 1*22 + 0*21 + 1*20 = 8 + 4 + 0 +1 = 1310
2x
Weights:
Most significant bit (msb)
ones
Binary system: Base 2
Positional value
(1011.101)2 = 23 + 21 + 20 + 2-1 + 2-3

## Slide 7
Number X in radix r system :
(x)r = xn-1xn-2 ... x1x0 . x-1 x-2 ... x-(m-1) x-m
Decimal Value of X :
Val10 = xn–1× r n–1 + xn–2× r n–2 + … + x1× r + x0 + x–1 × r–1 + x–2 × r–2 + … + x-m × r-m
Examples:
  (11011.01)2 = 1×24 + 1×23 + 0×22 + 1×2 + 1 + 0×2-1 + 1×2-2 = (27.25)10
  (2103)4 = 2×43 + 1×42 + 0×4 + 3 = (147)10
  (156.7)8 = (1x82 + 5x81 + 6x80 + 7x8-1 )10 = (64 + 40 + 6 + 0.875)10 = (110.875)10
  (55)9 = (45 + 5)10 = 5010
  (12)12 = (12 + 2)10 = 1410
Number system: generalization
position
radix

## Slide 8
When working with bits, oftentimes we have strings with 32 or 64 bits (a large number of bits!!).
So, it is more convenient and less error-prone to write the binary numbers in intermediate base systems such as Octal (base 8) or Hexadecimal systems (base 16),
Octal and Hex are often used in a digital system as sort of a “shorthand” way, more compact, to represent strings of bits.
However, it is important to keep in mind that digital circuits all work in binary.
Octal and Hex are simply used as a convenience for the humans involved.
Octal and hexadecimal systems (1)
Notes: Hexadecimal : Coined at IBM in 1963. From Greek hexi (six) and Latin decem (ten).

## Slide 9: Octal and hexadecimal systems (2)
Base 8 (octal) numbers : 0,1,2,3,4,5,6,7
  one octal digit is formed by grouping 3 bits.
Base 16 (Hexadecimal) is most useful as a “shorthand” notation for binary numbers.
Hex numbers : 0,1,2,3,4,5,6,7,8,9,A,B,C,D,E,F
  one hexadecimal digit is formed by grouping 4 bits and start with 0x
1000010101102 = 1000 0101 0110
= 8 5 6 16
1000010101102 = 100 001 010 110
= 4 1 2 6 8
= 0x 856

## Slide 10
Decimal | Binary | Octal | Hexadecimal
0 | 00000 | 000 | 00
1 | 00001 | 001 | 01
2 | 00010 | 002 | 02
3 | 00011 | 003 | 03
4 | 00100 | 004 | 04
5 | 00101 | 005 | 05
6 | 00110 | 006 | 06
7 | 00111 | 007 | 07
8 | 01000 | 010 | 08
9 | 01001 | 011 | 09
10 | 01010 | 012 | 0A
11 | 01011 | 013 | 0B
12 | 01100 | 014 | 0C
13 | 01101 | 015 | 0D
14 | 01110 | 016 | 0E
15 | 01111 | 017 | 0F
16 | 10000 | 20 | 10
Counting . . . 2, 8, 10, 16

## Slide 11
It’s quite tedious to work with only binary numbers…
In a group of bits, the least significant bit (lsb) is to the right. The most significant bit (msb) is to the left.
Within a word, the terms are the most significant byte (MSB) and the least significant byte (LSB).
10100001000001011110101101001101
10100001
01001101
00000101
11101011
Byte
Word (32-bit word)
Nibble
(Half-byte)
MSB
LSB
msb
lsb
Bytes, Nibbles, Words, MSB, LSB, …

## Slide 12
In digital computers, the range of numbers that can be represented is based on the number of bits available in the hardware structures that store and process information.
What is the total range of decimal values that can be represented in a single byte (8 bits)?
  minimum = 0000 0000 = 0
  maximum = 1111 1111 = 255
    Method 1: 1*27 + 1*26 + 1*25 + 1*24 + 1*23+ 1*22 + 1*21 + 1*20 = 255
    Method 2: 28 – 1 = 255
The maximum for n bits is 2n - 1
Range of values

## Slide 13: Conversion from/to base x

## Slide 14
Successive
Division
Weighted
Multiplication
Octal8
0 1 2 3 4 5 6 7
Successive
Division
Hexadecimal16
0 1 2 3 4 5 6 7 8 9 A B C D E F
Weighted
Multiplication
Successive
Division
Weighted
Multiplication
Binary2
0 1
Decimal10
0 1 2 3 4 5 6 7 8 9
Converting To and From Decimal
Notes: This slide first presents a graphical overview of the process for converting between DECIMAL↔BINARY (students should know how to do this) and then generalizes this process for converting between DECIMAL↔OCTAL & DECIMAL↔HEXADECIMAL.

## Slide 15
base X to Decimal Conversion
Any number in base 2, 8 or 16 can be converted to its decimal equivalent by multiplying each digit by its positional weight.
(127.4) 8 = 1 * 82 + 2 * 81 + 7 * 80 + 4 * 8-1 = (87.5)10
(11010) 2 = 1 * 24 + 1 * 23 + 0 * 22 + 1 * 21 + 0 * 20 = (26)10
(B65F)16 = 11 * 163 + 6 * 162 + 5 * 161 + 15 * 160 = (46687)10

## Slide 16
139
2
69
1
2
34
1
2
17
0
2
8
1
2
4
0
2
2
0
2
1
0
2
0
1
(139)10=(10001011)2
msb
lsb
Repeated Division Method
Divide the decimal number by 2.
Write the remainder after each division until a quotient of zero is obtained.
The first remainder is the lsb.
The last is the msb.
Example
Convert to binary (139)10
Decimal to Binary Conversion : Integer

## Slide 17: Convert to the binary 0.8110
0.8110 = 0.81 x 2 = 1.62
0.62 x 2 = 1.24
0.24 x 2 = 0.48
0.48 x 2 = 0.96
0.96 x 2 = 1.92
0.92 x 2 = 1.84
= 0.1100112 (approximately)
Decimal to Binary Conversion : Fraction
0.1 1 0 0 112
Repeated Multiplication Method
Multiply the fractional part by 2.
The digit to the left of the decimal point in the product will be 0 or 1 and contributes to the binary representation,
The fractional part of the product is used as the multiplicand in the next step.
Example

## Slide 18
Decimal to Octal/Hex Conversion
266
8
33
2
8
4
1
8
0
4
A decimal can be converted to octal (resp. hexadecimal) by using the same repeated-division method that used in binary conversion, but with a division factor of 8 (resp. 16) instead 2,
266 = (412)8
Example
423
16
26
7
16
1
10
16
0
1
423 = (1A7)16 = 0x1A7

## Slide 19
Octal to Binary
Replace each octal digit with its equivalent 3-bit binary sequence.
Example:
Binary to Octal
Make groups of 3 bits, starting from the binary point.
Add 0s to the ends of the number if needed.
Convert each bit group to its corresponding octal digit.
Example :
261.358 = 2 6 1 . 3 5 8
= 010 110 001 . 011 1012
10110100.0010112 = 010 110 100. 001 011 2
= 2 6 4 . 1 3 8
Binary and Octal conversions

## Slide 20
Hexadecimal to Binary
Replace each hex digit with its equivalent 4-bit binary sequence.
Example:
Binary to Hexadecimal
Make groups of 4 bits, starting from the binary point.
Add 0s to the ends of the number if needed.
Convert each bit group to its corresponding hex digit.
Example :
261.3516 = 2 6 1 . 3 516
= 0010 0110 0001 . 0011 01012
10110100.0010112 = 1011 0100. 0010 11002
= B 4 . 2 C16
1111
F
1011
B
0111
7
0011
3
1110
E
1010
A
0110
6
0010
2
1101
D
1001
9
0101
5
0001
1
1100
C
1000
8
0100
4
0000
0
Binary
Hex
Binary
Hex
Binary
Hex
Binary
Hex
Binary and Hex conversions

## Slide 21: Binary arithmetic

## Slide 22
1
1
+
10
1
0
+
1
0
1
+
1
0
0
+
0
11
1
1
+
1
The elementary operations are:
Compute 103+ 85
0 1 1 0 0 1 1 1
103

0 1 0 1 0 1 0 1

+
+ 85
188

0
1
0
1
1
1
1
0
1
1
1
1
Carry in
Carry out
1
Binary Addition

## Slide 23
1516
0A16
+
1F16
38
78
+
128
558
668
+
1438
258
128
+
378
6316
2D16
3616
+
Compute
A16
316
716
+
Octal and Hexadecimal Addition

## Slide 24
Notes:
  if multiplier bit is 1 copy multiplicand (place value)
    otherwise zero
  Note: need double length result
x 1 0 1 1
x 1 1 0 1
Multiplicand
0 0 0 0 
1 0 1 1  
1 0 1 1   
1 0 0 0 1 1 1 1
Multiplier
1 0 1 1
Binary Multiplication

## Slide 25
1 0
1 1
0
1 0 1 1 0
1 1
1 0
1 1
1 1
1
Quotient
Dividend
Remainder
Partial
Remainders
Divisor
Binary Division
1
1
1
1
0

## Slide 26
How do we subtract two binary numbers?
Equivalent to adding with a negative number
How can we represent negative numbers?
Binary Substraction
5 – 3 = ?
101 – 11 = ?
5 + (-3) = ?
101 + ? = ?
Sign/Magnitude
One’s complement
Two’s complement
Unsigned : 0, 1, 2, 3,…
Integer
Signed : ..,-2, -1, 0, 1, 2,..
Negative
Positive
(139)10=(10001011)2
(-139)10=(?)2
(+139)10=(?)2
Presentation including the sign bit
materially

## Slide 27
Let msb represent the sign (0=positive, 1=negative)
and the remaining N-1 bits for magnitude
  0111 = 7
  1111 = -7
Problems
  Two zero’s: +010 (00002) different than -010 (10002)
  Addition does not work
0 0 1 02
1 1 0 12

+
- 510
-310
210
+
1 1 1 12
=-710
Sign/Magnitude Representation

## Slide 28
Leading 0’s for positive and 1’s for negative
Negative numbers: complement the positive number
  Example:
    +710 : 01112
    -710 : 10002
Problem
  Two zero’s still: +010 (00002) different than -010 (11112)
One’s complement

## Slide 29
The 2’s-complement system for representing signed numbers works like this:
If the number is positive, the magnitude is represented in its true binary form, and a sign bit of 0 is placed in front of the MSB.
If the number is negative, apply the 2’s complement form :
  Obtain the bit pattern of positive counterpart,
  Invert the bit pattern (1’s complement),
  Add one to it.
Two’s complement
+ 45 = 0 1 0 1 1 0 1
0 1 0 1 1 0 1 = + 45
1 0 1 0 0 1 0
1 0 1 0 0 1 1 = - 45
+ 1

## Slide 30
Two’s complement : examples
Two’s complement
(-9)10 = (?)2
(-9)10 = 2’s complement (+9) = 2’s complement (01001)
= 10110 + 1 = 101112
(10111)2 = (?)10
(10111)2 = - ( 2’s complement (10111))
negative
= - ( 01000 + 1)
= - ( 01001)
= - 910
(00111)2 = (?)10
(00111)2 = + (1*22 + 1*21 + 1*20 )
positive
= + 710
represented in 5 bits

## Slide 31
Range of values
Unsigned integer
0, 1, 2, 3..
Integer Decimal
Signed integer
.., -2, -1, 0, 1, 2,..
Range values : [0, 2n – 1]
Presentation : true binary form
Presentation : 2’s complement
Range values : [- 2n-1, 2n-1 - 1]
(n bits)
4 bits
[0, 15]
0000
0001
…
1111
= 0
= 1
= 15
[- 8, 7]

## Slide 32
Binary | Decimal
0000 | 0
0001 | 1
0010 | 2
0011 | 3
0100 | 4
0101 | 5
0110 | 6
0111 | 7
1000 | -8
1001 | -7
1010 | -6
1011 | -5
1100 | -4
1101 | -3
1110 | -2
1111 | -1
Positive numbers
are represented as usual.
Negative numbers are
listed in reverse order.
Can represent one more
negative number than
positive numbers.
All negative numbers
have msb set. This is
called the sign bit.
Only one number represent 0
4 bits Two’s complement signed integer

## Slide 33
Signed vs Unsigned Number Wheels

## Slide 34
Rules for addition
  Use the signed number notation with negative numbers in 2’s complement form
  Add the two signed numbers.
  Discard any final carries.
  The result is in signed form.
11111111 = -1
11111000 = -8
11110111
= -9
1
Discard carry
00001110 = +14 11101111 = -17
11111101
= -3
00011110 = +30
00001111 = +15
00101101
= +45
Arithmetic Operations with Signed Numbers

## Slide 35
Sometimes result can’t be represented with given number of bits
Either too large magnitude of positive or negative
Oveflow occurs only if both numbers have the same sign.
Example 1 : For 4-bit representation
  0111+0001 = 1000 WRONG
  1000 in two’s complement is -8, not +8
Example 2: For 8-bit representation
The overflow  Sign bit of the result different than the sign bit of the two added numbers.
10000001 = -127
10000001 = -127
00000010
= +2
1
Discard carry
01000000 = +64
01000001 = +65
10000001
= -127
X
X
Overflow

## Slide 36
Our decimal system handles Two types of non-integer real numbers
  fixed point
    Using the decimal point (.) to make a notation:
    3.78 = 3.103 + 7.10-1 + 8.10-2
  floating point (called also scientific notation)
    Used to represent very large and very small numbers (integer or real), with the precision needed
    Unit of electric charge e = 1.602 176 462 x 10-19 Coulomb
    Volume of universe = 1 x 1085 cm3
Real numbers

## Slide 37
4 specifications required for a number
  Sign
  Magnitude or mantissa or Significand
  Sign of the exponent
  Magnitude of the exponent
Plus
  Base of the exponent
  Location of decimal point (or other base) radix point
Sign of the exponent
- 0.83569 x 10-7
Magnitude of the Exponent
Base of the Exponent
Mantissa
Sign of the mantissa
Location of decimal point
Floating point numbers

## Slide 38
The following representations are all the same in value
  + 0.110  25
  + 0.00110  27
  + 11000000  2(-3)
Floating-point numbers should be normalized
Idea
  Exactly one non-zero digit should appear before the point
    In a binary number, this digit should be 1
  Normalized: -1.101101×2–3
  Not Normalized: 1101.101×2–6
Floating-point numbers normalization

## Slide 39
We mimic the decimal floating point notation to create a “hybrid” binary floating point number:
  We first use a “binary point” to separate whole numbers from fractional numbers to make a fixed point notation:
      e.g. 00011001.110
  We then “float” the binary point:
      00011001.110 => 1.1001110 x 24 (mantissa = 1.1001110, exponent_value = 4)
  Now we have to express this without the extra symbols ( x, 2, . )
      by convention, we divide the available bits into three fields: sign, mantissa, exponent
sign | exponent | mantissa
Real numbers in binary

## Slide 40
For a normalized floating point number (S, E, F)
Significand is equal to (1.F)2 = (1.f1f2f3f4…)2
  IEEE 754 assumes hidden 1. (not stored) for normalized numbers
  Significand is 1 bit longer than fraction
Value of a Normalized Floating Point Number:
 (1.F)2 × 2exponent_value
 (1.f1f2f3f4 …)2 × 2exponent_value
 (1 + f1×2-1 + f2×2-2 + f3×2-3 + f4×2-4 …)2 × 2exponent_value
  S = 0 is positive, S = 1 is negative
S
E
F = f1 f2 f3 f4 …
Normalized Floating Point Numbers

## Slide 41
Found in virtually every computer invented since 1980
Single Precision Floating Point Numbers (32 bits)
  1-bit sign + 8-bit exponent + 23-bit fraction
Double Precision Floating Point Numbers (64 bits)
  1-bit sign + 11-bit exponent + 52-bit fraction
S
Exponent (8bits)
Fraction (23 bits)
S
Exponent (11bits)
Fraction (52 bits)
IEEE 754 Floating-Point Standard

## Slide 42
How to represent a signed exponent?
  Sign + magnitude representation for the exponent,
  Two’s complement representation,
  Biased representation
IEEE 754 uses biased representation for the exponent
  Exponent Value = E– Bias (Bias is a constant)
Value of a Normalized Floating Point Number is
 (1.F)2 × 2(E-Bias)
 (1.f1f2f3f4 …)2 × 2(E-Bias)
 (1 + f1×2-1 + f2×2-2 + f3×2-3 + f4×2-4 …)2 × 2(E-Bias)
S = 0 is positive, S = 1 is negative
Exponent Representation

## Slide 43
Single precision
  The exponent field is 8 bits
  E = 0 and E = 255 are reserved for special use
  E = 1 to 254 are used for normalized floating point numbers
  Bias = 127 (half of 254)
  Exponent value = E – 127 Range: -126 to +127
Double precision
  The exponent field is 11 bits
  E = 0 and E = 2047 are reserved for special use
  E = 1 to 2046 are used for normalized floating point numbers
  Bias = 1023 (half of 2046)
  Exponent value = E – 1023 Range: -1022 to +1023
Biased Exponent

## Slide 44
What is the decimal value of this Single Precision float?
Solution:
  Sign = 1 is negative
  E = (01111100)2 = 124, E – bias = 124 – 127 = –3
  Significand = (1.0100 … 0)2 = 1 + 2-2 = 1.25 (1. is implicit)
  Value in decimal = –1.25 × 2–3 = –0.15625
What is the decimal value of?
Solution:
  Value in decimal = +(1.01001100 … 0)2 × 2130–127 =
  (1.01001100 … 0)2 × 23 = (1010.01100 … 0)2 = 10.375
1
0
1
1
1
1
1
0
0
0
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
0
0
0
0
0
1
0
0
1
0
0
1
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
implicit
Examples of Single Precision Float

## Slide 45
What is the decimal value of this Double Precision float ?
Solution:
  Value of exponent = (10000000101)2 – Bias = 1029 – 1023 = 6
  Value of double = (1.00101010 … 0)2 × 26 (1. is implicit) =
  (1001010.10 … 0)2 = 74.5
What is the decimal value of ?
Do it yourself! (answer should be –1.5 × 2–7 = –0.01171875)
0
1
0
0
0
0
0
0
0
1
0
1
0
0
1
0
1
0
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
0
1
1
1
1
1
1
1
0
0
0
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
Examples of Double Precision Float

## Slide 46
Convert - 0.8125 to single and double-precision floating-point
Solution:
  Fraction bits can be obtained using multiplication by 2
    0.8125 × 2 = 1.625
    0.625 × 2 = 1.25
    0.25 × 2 = 0.5
    0.5 × 2 = 1.0
    Stop when fractional part is 0, or after computing all required fraction bits
  Fraction = (0.1101)2 = (1.101)2 × 2 –1 (Normalized)
  E = –1 + Bias = 126 (single precision) and 1022 (double)
0.8125 = (0.1101)2
1
0
1
1
1
1
1
1
0
1
0
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
0
1
1
1
1
1
1
1
1
1
0
1
0
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
Single Precision
Double Precision
Decimal to Binary Floating-Point

## Slide 47
Single-Precision | Exponent = 8 | Fraction = 23 | Value
Normalized Number | 1 to 254 | Anything | ± (1.F)2 × 2E – 127
Denormalized Number | 0 | nonzero | ± (0.F)2 × 2–126
Zero | 0 | 0 | ± 0
Infinity | 255 | 0 | ± ∞
NaN (not a Number) | 255 | nonzero | NaN
Double-Precision | Exponent = 11 | Fraction = 52 | Value
Normalized Number | 1 to 2046 | Anything | ± (1.F)2 × 2E – 1023
Denormalized Number | 0 | nonzero | ± (0.F)2 × 2–1022
Zero | 0 | 0 | ± 0
Infinity | 2047 | 0 | ± ∞
NaN | 2047 | nonzero | NaN
Summary of IEEE 754 Encoding

## Slide 48: Other codes

## Slide 49
In the Binary Coded Decimal (BCD) representation each decimal digit is converted to its 4-bit pure binary equivalent
This code is the simplest, most intuitive binary code for decimal digits and uses the same powers of 2 as a binary number,
  but only encodes the first ten values from 0 to 9.
    For example: (57)dec  (?) bcd
    ( 5 7 ) dec = (0101 0111) bcd
Binary Coded Decimal (BCD)
Notes: Answer 1: 6
Answer 2: 1010, 1011, 1100, 1101, 1110, 1111

## Slide 50
You can think of BCD in terms of column weights in groups of four bits. For an 8-bit BCD number, the column weights are:
80 40 20 10 8 4 2 1
What are the column weights for the BCD number : 1000001101011001?
1000 0011 0101 1001
  8000 4000 2000 1000 800 400 200 100 80 40 20 10 8 4 2 1
Note that you could add the column weights where there is a 1 to obtain the decimal number. For this case:
  1000001101011001 = 8000 + 200 +100 + 40 + 10 + 8 +1 = 835910
Binary Coded Decimal (BCD)

## Slide 51
Add the following BCD numbers :
  0011 + 0100
  010001010000 + 010000010111
  1001 + 0100
Solution
  0011+0100=0111
  010001010000+010000010111=100 0110 0111
  1001+0100=0001 0011 (Add 6 to the invalid BCD number which is >9)
BCD addition

## Slide 52
The Gray code is used in applications where numbers change rapidly.
  Only one bit changes from each value to the next.
  This allows to avoid problems in systems where an error can occur if more than one bit changes at a time
Three bit binary and Gray code equivalents.
Gray code

## Slide 53
  Three IR emitter/detectors are used to encode the position of the shaft.
  The encoder on the left uses binary and can have three bits change together, creating a potential error.
  The encoder on the right uses gray code and only 1-bit changes, eliminating potential errors.
Binary sequence
Gray code sequence
Example of application: A shaft encoder
Gray code :

## Slide 54
Copyright ©2007 by Pearson Education, Inc. Columbus, OH 43235 All rights reserved.
Decimal-Binary-Hex-BCD-Gray

## Slide 55
The ASCII code represents characters and functions on a computer keyboard
  26 lowercase
  26 uppercase letters
  10 digits
  7 punctuation marks
  20 to 40 other characters.
Seven bit code: 27 = 128 possible codes
use: transfer information between computers; computers & printers;
Extension: In 1981, IBM introduced extended ASCII, which is an 8-bit code and increased the character set to 256
Copyright ©2007 by Pearson Education, Inc. Columbus, OH 43235 All rights reserved.
ASCII (American Standard Code for Information Interchange)

## Slide 56
ASCII code

## Slide 57
ASCII code

## Slide 58
UNICODE extends ASCII to 65,536 universal characters codes
  For encoding characters in world languages
  Available in many modern applications
  2 byte (16-bit) code words
UNICODE

## Slide 59
Do NOT mix up "conversion of a decimal number to a binary number" with "coding a decimal number with a binary code".
1310 = 11012
  This is conversion
13  0001 0011BCD
  This is coding
Conversion or Coding?